## Slide 1: Computational Science An Industrial Perspective Workshop Multiscale Modeling for the Development of Commercial Materials and Devices
Dr. Edward Furlani
Dept. of Chemical and Biological Engineering Dept. Electrical Engineering

## Slide 2: Interdisciplinary Computational Research
Academic Research: SUNY at Buffalo (2011 - present )
Prof. Chemical and Biological Engineering
Prof. Electrical Engineering
Industrial Research: Eastman Kodak Research Labs (1982 – 2010) Computational modeling for commercial product development.
    Research Areas
    Nanophotonics: plasmonics, photothermal phenomena, metamaterials
    Computational fluid dynamics (CFD): multiphase systems, heat/mass transfer, nanofluids, ink jet systems
    Microfluidics: devices and processes, design and simulation
    Computational Magnetics: Directed self-assembly, bioseparation, drug delivery
    MOEMS/MEMS: design and simulation
Dr. Edward Furlani (efurlani@buffalo.edu)
Notes: Prof. Furlani has joint appointments in the Depts. of Chemical and Biological Engineering and Electrical Engineering. His research involves multidisciplinary/multiscale modeling with an emphasis on the development of novel materials and devices. Current projects include:
Development of microfluidc–based optical biosenors
Development of polymer-based metamaterials using laser writing techniques.
Analysis of plasmon-enhanced photothermal energy conversion with an emphasis on cancer therapy.
Development and application of hybrid magneto-plasmonic nanostructures for biomedical applications such as targeted drug delivery and photo-induced hyperthermia.
Development of magnetic nanoparticle enhanced Surface Plasmon Resonance based biosensors. The magnetic particles enable accelerated field-directed trapping of the target biomaterial on the sensing element.

## Slide 3: Presentation Overview
Introduction
  Modeling Overview
  Kodak Materials and Micro-Device Research
Micro-Optical Electro-Mechanical Devices
Microfluidics: Inkjet Technology
Summary

## Slide 4: Multiscale Modeling
Modeling Phenomena Across Multiple Length and Time Scales

## Slide 5: Interdisciplinary Computational Research
Plasmonic Photothermal Phenomea
Particle- Fluid Interactions
EM Nanoparticle
Properties
EM Fluid Properties
Computational Electromagnetics
& Photonics
Computational Fluid Dynamics & Microfluidics
Nanofluids
Mass Transport & Self-Assembly
Nanomagetics Self-assembly

## Slide 6: Modeling Overview
Micro Nozzle Array
Microfluidics
InkJet
Micro-Optical
Electro-Mechanical
Devices
Nanofluids Mass Transport
MEMS Light Modulator
Inkjet Printing
60 nm
Pigment
Inkjet Printing
Nanofluids

## Slide 7: Kodak Materials & Microdevice Research
Interdisciplinary Research Team
(4-12 Contributors)
Concept Development Performance Metrics
Intellectual Property
Fundamental Modeling & Design
Fabrication & Characterization
Commercialization
Clean Room Prototype Fabrication $50-200K per Design Cycle 1-3 Month Turn Around
Notes: 7

## Slide 8: Materials & Microdevice Research
Clean/Wet Etch
  Megasonics cleaner
  Spin spray rinser/dryer
Deposition
  CVC sputterer
  LPCVD furnace
  PEO annealing furnace
Lithography
  Canon stepper
  Spin coater
  Polyimide/PMDS ovens
Dry Etch
  Oxford etcher
  Dielectric Etch
STS
  STS cluster tool
  Wafer grinder
Analytical
  Ellipsometer
  Reflectrometer
  SEM
  Profilometer
Processing: 6” (150mm) Si wafers
Resolution: 0.5µm features
Full CMOS* Integration
In House Prototype Development Facility 12,000 sq ft Class 100/1000 Clean Room
*CMOS = Complementary Metal–Oxide–Semiconductor

## Slide 9: Micro-Optical Electro-Mechanical Devices
Kodak MEMS Light Modulator
Micromachined Reflection Grating
Motivation: Solid State Display Applications
L  100 m
W  50 m
115 in Front Projection Display

## Slide 10: Micro-Optical Electro-Mechanical Analysis
On Pixel
Off Pixel
On Pixel
Off Pixel
*M. Kowarz, Spatial light modulator with conformal grating device, US. Patent 6307663, 2001.
W  50 m
L  100 m
Linear Pixel Array
Kodak GEMS* Technology (Grating Electromechanical System)
Modeling and Device Design

## Slide 11: Display Applications: Linear Array Operation
Enlarged View 20 Pixels
Pixel #1 ON
Pixel #2 OFF
Pixel #3 ON
Pixel #4 OFF
Pixel #5 ON
Pixel #6 ON
Enlarged View 6 Pixels
GEMS Light Modulator

## Slide 12: Commercial Projection Display
Front Projection System
Galvanometer Mirror
X-cube
GEMS
GEMS
GEMS
Front projection Systems
Rear projection laser TV
Heads-up displays
Laser Printing
Applications
Photograph of Scene from Scanned Motion Picture Film
115 in Front Projection Display

## Slide 13: Device Analysis and Rational Design
Operating Voltage?
Microbeam Deformation Profile?
Diffraction Efficiency?
Dynamic Response of Microbeam?
On Pixel
Off Pixel
W  50 m
L  100 m

## Slide 14: Length and Time Scales
SEM: Gap Beneath Microbeam
150 - 200 nm
Mean free path of air molecules beneath microbeam = 65 nm!
Nanoscale
200 nm
Mesoscale (mm)
Length
20 m
Microscale
Time
Microbeam Response Time = 30 ns
30 ns
200 nm
Si3Ni4

## Slide 15: Electrostatic Deformation of Microbeam
T = Tensile Force in Si3Ni4 E = Young's Modulus I = Moment of Inertia
Nonlinear Electrostatic Force per Length
Si3Ni4
Predict
Deformation Profile vs. Activation Voltage
Pull-In Voltage

## Slide 16: Predict Deformation of Microbeam
*E. P. Furlani, Analysis of grating light valves with partial surface electrodes, J. Appl. Phys. 83 1998.
Nonlinear ODE
Self-Consistent Green’s Function Analysis*
A
C
B
Boundary Conditions

## Slide 17: Microbeam Deformation: Model vs. Experiment
E. P. Furlani, Analysis of grating light valves with partial surface electrodes, J. Appl. Phys. 83 1998
Predicted Microbeam Profile y(x) vs. AFM
y(x)
Optimization
Activation Voltage: Theory vs. Experiment

## Slide 18: Optical Diffraction Efficiency
Scalar Diffraction Theory
Diffraction Efficiency
y(x)
x
Trapezoidal Microbeam Profile

## Slide 19: Dynamic Analysis
Continuum Model
Coupled Electrostatic/Structural/Gas Flow Analysis
Coupled Structural Analysis & Gas Dynamics
Bending & Tension
Gas - Damping & Compression
Coupling: Gas Flow Influences Microbeam Dynamics
Spring
Lumped-Element Model Damped Spring/Mass System

## Slide 20: Continuum to Lumped-Element Model
Continuum Analysis y(x) = displacement along microbeam
Lumped-Element Analysis y = displacement of midpoint of microbeam
Bending & Tension
Lumped-Element Model Damped Spring/Mass System
Gas - Damping & Compression
Spring
E. P. Furlani, Theory and simulation of viscous damped reflection phase gratings, J. Phys. D: Appl. Phys. 1999.

## Slide 21: Lumped-Element Dynamic Analysis
E. P. Furlani, Theory and simulation of viscous damped reflection phase gratings, J. Phys. D: Appl. Phys. 1999.
Effective Viscosity
Mean free path of air molecules beneath microbeam  65 nm!
Knudsen number
Linearized Reynolds Equation (Compressible Gas)
Time Harmonic Analysis
Gas Damping
Gas Compression

## Slide 22: Effective Modeling Parameters
Applied Voltage
V(t)
t
0 = fundamental frequency
1 = first harmonic

## Slide 23
Lumped-Element Model vs. Experiment
E. P. Furlani & M. Kowarz, Optical Data Modulation System with Self-damped Electromechanical Conformal Grating, US Patent, 2002.
Prediction of Diffraction Intensity into 0'th Order vs. Applied Voltage
Applied Voltage
Diffraction Intensity (Experiment)
Diffraction Intensity (Theory)
0’th Order Diffraction Intensity
Applied Voltage

## Slide 24: Summary
Operating Voltage
Microbeam Deformation Profile
Diffraction Efficiency
Dynamic Response of Microbeam
On Pixel
Off Pixel
W  50 m
L  100 m

## Slide 25: Microfluidics: Inkjet Printing
Continuous Printing
Drop-on-Demand (DOD) Printing
30,000 Drops Generated per sec from each Nozzle
500,000 Drops Generated per sec from each Nozzle
Microfluidic-based Printing: Most Successful Microfluidic Application ($50-100B)
Motivation
Notes: 25

## Slide 26: Microfluidics: Inkjet Technology
Micro Nozzle Array
Continuous Printing
Drop-on-Demand (DOD) Printing
Notes: 26

## Slide 27: Fluid Dynamics and Transport Phenomena
Thermal Properties of Fluids
Mass Transport
Diffusion & Advection of Molecules/Nanoparticles
Particle/Fluid Interactions (Nanofluids)
Thermal Effects of Fluid Constituents
Fluid Dynamics
Constitutive Relation
Thermal Analysis

## Slide 28: Historical Contributions to Fluid Mechanics
Archimedes
(C. 287-212 BC)
Newton
(1642-1727)
Leibniz
(1646-1716)
Euler
(1707-1783)
Navier
(1785-1836)
Stokes
(1819-1903)
Reynolds
(1842-1912)
Prandtl
(1875-1953)
Bernoulli
(1667-1748)
Taylor
(1886-1975)

## Slide 29: Hydrodynamics
Governing Equations based on the Laws of Physics
  Conservation of Mass ( = fluid density, u = fluid velocity).
  Newton’s Second Law: the change of momentum equals the sum of forces (p = pressure, µ = viscosity, f = external force density).
  Conservation of Energy - First Law of Thermodynamics (T= fluid temperature)
Notes: We treat all properties as averages over a suitably large number of molecules.
A small element of fluid, a fluid particle or fluid point, is the smallest element of fluid
whose macroscopic properties are not influenced by individual molecules.

## Slide 30: Navier-Stokes Equations
3D Cartesian Coordinates
Convection
Pressure gradient
Viscous terms
Local Acceleration
The Navier Stokes equations are very difficult to solve analytically because they are non-linear. Analytical solutions exist for few albeit very important cases such laminar flow through regularly shaped conduits!
Claude Navier
1785-1836
Georges Stokes
1819-1903
  Newton’s Second Law: change of momentum equals the sum of forces (p = pressure, µ = viscosity, f = external force density).

## Slide 31: Numerical Approach to Solving PDEs
Governing Equations ICS/BCS
Discretization
System of Algebraic Equations
Equation (Matrix) Solver
Approximate Solution
Continuous Solutions
Finite-Difference
Finite-Volume
Finite-Element
Spectral Methods
Boundary Element
Discrete Nodal Values
Tridiagonal
ADI
SOR
Gauss-Seidel
Conjugate gradient
Gaussian elimination
ui (x,y,z,t)
p (x,y,z,t)
T (x,y,z,t)

## Slide 32: What is Computational Fluid Dynamics (CFD)?
Computational fluid dynamics (CFD) is the science of predicting the behavior of fluid flow and related transport phenomena, e.g. heat transfer, chemical kinetics etc., by solving the governing equations using numerical methods.

## Slide 33: CFD Modeling Cycle
Device Concept Develop CAE Model
Governing Equations Discretization - Mesh Generation
Algebraic System
of Equations
Choose Solution Algorithm
Solution and Post Processing Data Analysis - Interpretation
Computational Mesh
Piston Driven Droplet Generation
Notes: 33

## Slide 34: CFD Program Solution Cycle

## Slide 35: CFD Analysis Applied to Inkjet Printing
Inkjet Printing Methods (DOD & CIJ)
Phase Change Simulation
Thermal-Fluidic & Free-Surface Analysis
    Droplet Generation
    Marangoni-Assisted Jet Instability
Particle-Fluid Interactions
    Aerodynamic Analysis
    Nanofluids
Fluid-Surface Interactions
Notes: 35

## Slide 36: Microfluidic-based Printing
Continuous Printing
Drop-on-Demand (DOD) Printing
30,000 Drops Generated per sec from each Nozzle
500,000 Drops Generated per sec from each Nozzle
Notes: 36

## Slide 37: Emerging Microfluidic Printing Applications
Photovoltaics
Fuel Cells
Batteries
Flex circuits
Smart Textiles
PCB Photomasks
Interconnects
Flat Panel Display
PLED
LCD
Color filters
Flexible displays
RF- ID
Antennas
Printed Circuit Boards
Smart Packaging

## Slide 38: Coating of Stents
Current coating methods: dipping, ultrasonic spray coating, painting (air brush), and deposition along the struts using syringes.
Stent - fabricated from metals/alloys/polymers and surface treated with materials that reduce the rejection mechanisms.
Ink-jet based Stent coating

## Slide 39: Multiphase Computational Fluid Dynamics (CFD)
Tracking an Interface
Eulerian Methods (Fixed Grid)
Lagrangian Methods (Adaptive Grid)
Volume of Fluid (VOF) Method*

## Slide 40: Drop-on-Demand Printing Thermal Bubble Jet
Ink
Heater
Orifice
Vapor Bubble
Pressure Chamber
Heater pulse duration
  250 ns
0
t
…
V(t)

Notes: 40

## Slide 41: Printing Cartridge - Thermal Bubble Jet
FILTER
FLAT CABLE
SEALING GLUE
ACTUATOR GROUP
PROTECTIVE GLUE
LID
INK “RETAINER”
ADHESIVE
TRANSFER
INK TANK
Protective Layer
Nozzle Plate
Hydraulic circuit
Ink Drop
Silicon Substrate
Vapour Bubble
Thin Film Heater

## Slide 42: Kodak MEMS Thermal Bubble Jet Drop Ejector
Voltage Applied to
Ta-Si-N Heater Layer
Ta-Si-N Heater Layer < 0.1 m
Ink
Ta
Silicon Oxide
Silicon Nitride
Silicon
Ta-Si-N
0
t
…
V(t)

Heater pulse duration:   250 ns
Notes: 42

## Slide 43
Thermal Bubble Jet Drop Ejection: Model vs. Experiment
3D CFD Phase Change Analysis
Homogeneous Bubble Nucleation & Free-Surface Tracking
Quad-Core Workstation 2.8 GHz Processors Windows XP 32 Bit
Simulation Time = 24 Hrs
Flow 3D - VOF Solver
Notes: 43

## Slide 44: CFD Thermal Bubble Jet Simulation
Power is applied to a thin film resistive heater.
Fluid adjacent to the heated structure reaches its superheat limit and a vapor bubble form.
The bubble expands rapidly, driving fluid through the orifice causing a droplet to be expelled.
As the vapor bubble expands, a thin layer of superheated fluid which feeds the vapor bubble is depleted, causing the bubble growth to slow, and eventually collapse.
Predicted Volume 6.8pl
Predicted Velocity 16.5m/s

## Slide 45: DOD Simulation vs. Experiment

## Slide 46: Understanding Air Entrapment - Moving Bubbles
Trapped Air Bubbles

## Slide 47: Moving Bubbles
Moving Bubble

## Slide 48: Moving Bubbles
Moving Bubble

## Slide 49: Bubble Movement (3D CFD)
Contact Angle = 90 deg
Contact Angle = 135 deg

## Slide 50: Kodak Stream Technology
Image Quality
Commercial Printer
Micro Nozzle Array
Printer
Moving Substrate (500-1000 ft/min)
Prints 8x11in Full Color Image in 1 ms
2400 Times Faster Than Home Printer*
60 nm
Colored Pigment Nanoparticles
*Assumes 25 color pages printed per minute
Notes: What could be considered the third generation of CIJ, called Stream technology represents a revolutionary jump in CIJ. You have unparalled speed at offset-class image quality.
The ability to not only print on the usual types of bond papers but to print on coated glossy papers with excellent image quality.
Actual output from a technology demo at drupa 2008 is shown on coated glossy stock
The arrays can be scaled to nearly any length and the high reliability and availability that CIJ has been known for is maintained.

## Slide 51: Thermally Induced Microdrop Generation
J. M. Chwalek, et al. Phys. of Fluids 14, 37-40, 2002
Micro Nozzle Array
Heater Embedded in Nozzle

## Slide 52: Kodak CMOS/MEMS Array Microdrop Generator
Ink Feed Channels
Orifice Diameter = 10 µm
Array of Nozzles
300 µm
Ink channels etched into a CMOS wafer
Orifice
Ink inlet
30 µm
Heater Cross-section

## Slide 53: CFD Analysis of Microdrop Generation
V(t)
0

t
…
*FLOW 3D - VOF Solver
Coupled Thermal-Fluidic & Free-Surface Analysis*
Quad-Core Workstation 2.8 GHz Processors Windows XP 32 Bit 8 GB RAM
Simulation Time = 36 Hrs

## Slide 54: Microdrop Generation: Model vs. Experiment
No Fitting Parameters!
Simulation Time = 36 Hrs
CFD Simulation
Strobbed Image of Drop Formation
Fluid = H2O
Too Long for Design and Optimization of Devices!
20 m

## Slide 55: Length and Time Scales
60 nm
Colored Pigment Nanoparticles
Length
cm
Nozzle Array
mm
Microjet
Time
 = 2 s
Modulation Voltage
f = 500 kHz
 = 30-50 s
Jet Break Up L = 600-1000 m
 = 250-350 s
V = 20 m/s
Paper
Drop to Paper L = 5-7 mm
Drop
20 m
Volume = 3.5 pl 106 particles

## Slide 56
Drop Size Selection - Air Deflection
Air Stream
20 m
Notes: 56

## Slide 57: Performance Optimization
Optimize Voltage Waveform:
Control jet Breakup Length
Control Drop Volume & Velocity
Maximize Drop Generation Frequency
Suppress Satellite Drops
Slender Jet Analysis Simulation Time = Minutes
CFD Simulation = 36 Hrs Awkward for Optimization

## Slide 58: Slender Jet Analysis
L
D
E. P. Furlani and M. S. Hanchak, Nonlinear Analysis of the Deformation and Breakup of Viscous Microjets using the Method of Lines, Int, J. Numerical Methods in Fluids, on line, March 2010.
hi-1
pi-1
Ti-1
hi
pi
Ti
hi+1
pi+1
Ti+1
z
0
vi
vi+1
vi-1
Method of Lines

## Slide 59: Slender Jet Analysis vs. Experiment
Experiment
Model
Experiment
Model
Simulation Time 10-20 min*
*Programmed in Matlab using ODE Solvers
M. Hanchak and E. P. Furlani, Numerical Analysis of Droplet Formation in Thermally Modulated Viscous Microjets, in preparation, 2010.
Notes: 59

## Slide 60: Particle-Fluid Interactions
Vz (cm/s)
Monitor Particle Count in Nozzle
Flow of Pigment Particles Through Orifice
60 nm
Pigment Nanoparticles
Vz (cm/s)
Fluxuation in Particle Count
Pigment Fluxuations Cause Undesired Image Artfacts

## Slide 61: Particle-Fluid Interactions Aerodynamic Droplet Interaction

## Slide 62: Fluid-Surface Interaction
Coalescence: Multiple Drops Impacting a Surface

## Slide 63: Translational Research
Industrial Grants and Contracts*
2014-2015: Multiscale modeling of Magnetohydrodynamic-based Liquid Metal Jet 3D Printing
2014-2015: Electromagnetic Modeling for Development of Inductive Loop Technology for Automobile Sensing
2013-2014: Process and Materials Modeling involving Thermal and Gas Dynamics for Novel Green Energy Technology based on a Knudsen Compressor.
2013-2014: Development of computational fluid dynamic (CFD)-based device and process modeling:
  Design of custom commercial apparatus and processes.
  Coupled heat and mass transfer (flow dynamics) of highly viscous liquid-based, granular and structurally deformable materials.
Remote Sensing
Additive Manufacturing
Energy Harvesting
Equipment Design
*Partial support from NYS High Performance Computing Consortium (HPC2)

## Slide 64: Translational Research
Industrial Grants and Contracts
2011-1212: CFD Modeling of Colloidal and Wetting Phenomena in Porous Media for Development of Commercial Pigmented Ink Formulations for Ink Jet Printing
2011-1212: Thermo/Gas Dynamics Modeling of Chemical Reactor and Reaction Process for Synthesis of Si Nanowires.
2013: Process and Materials Modeling Involving Thermal/Fluidic/Phase Change Analysis for Novel Commercial Lyophilization (Freeze-Drying) Systems for Pharma Industry.
2010-1211: CFD Modeling of Rotary Blood Pump Dynamics and Performance of Aortic Valve Heart Assist Device.
Pump Impeller
Droplets Impacting Porous Media
Continuous-Drop Freeze Drying System
Simulation of Drop Generation
Model of Impeller Dynamics
Pharma
Nanofluids - Inks
Nanoparticle Synthesis
Biotechnology

## Slide 65: Summary
Interdisciplinary multiscale modeling is used in industry:
  Advance fundamental understanding of new processes, materials and devices
  Enable rational design and optimization
  Accelerate development cycle of commercial products
Multicore workstations and high performance computer facilities are becoming more cost effective and accessible for large scale simulations
Public domain and commercial software is becoming more available, adaptable and increasingly sophisticated to facilitate analysis.
Significant challenges and opportunities exist for the development of novel algorithms for modeling coupled phenomena across multiple length and time scale.